## Slide 1: GPAGER 전류 측정

## Slide 2
Device | Status
LCD Backlight | On
LCD Display | On
GPS | On
Buzzer | Off
Vibrator | Off
LoRa Send | Off
LoRa Receive | Off
1. Average Current : 83.44 mA

## Slide 3
Device | Status
LCD Backlight | Off
LCD Display | Off
GPS | On
Buzzer | Off
Vibrator | Off
LoRa Send | Off
LoRa Receive | Off
2. Average Current : 81.08 mA

## Slide 4
Device | Status
LCD Backlight | On
LCD Display | On
GPS | Off
Buzzer | Off
Vibrator | Off
LoRa Send | Off
LoRa Receive | Off
3. Average Current : 30.67 mA

## Slide 5
Device | Status
LCD Backlight | Off
LCD Display | Off
GPS | Off
Buzzer | Off
Vibrator | Off
LoRa Send | Off
LoRa Receive | Off
4. Average Current : 27.42 mA

## Slide 6
Device | Status
LCD Backlight | On
LCD Display | On
GPS | On
Buzzer | Off
Vibrator | Off
LoRa Send | On
LoRa Receive | Off
5. Current : 107.70 mA

## Slide 7
Device | Status
LCD Backlight | Off
LCD Display | Off
GPS | On
Buzzer | Off
Vibrator | Off
LoRa Send | On
LoRa Receive | Off
6. Current : 106.05 mA

## Slide 8
Device | Status
LCD Backlight | On
LCD Display | On
GPS | Off
Buzzer | Off
Vibrator | Off
LoRa Send | On
LoRa Receive | Off
7. Current : 50.17 mA

## Slide 9
Device | Status
LCD Backlight | Off
LCD Display | Off
GPS | Off
Buzzer | Off
Vibrator | Off
LoRa Send | On
LoRa Receive | Off
8. Current : 47.38 mA

## Slide 10
8. Power OFF Average Current : 1.55 mA